TEL:886-2-2601-3311

FAX:886-2-2601-3898

NO.4 Lane 505, Zhongzheng Rd,. Linkou Shiang,Taipei, Taiwan 24445 . R.O.C

Magnetic Buzzer

PB-0925ME-05Q

(RoHS)                   DATE:2009.03.02

1﹒Electrical Characteristics                              VER .:3

| Oscillation Frequency (Hz) | 2500 |
| --- | --- |
| Operating Voltage (Vp-p) | 4.0 ~ 7.0 |
| Rated Voltage (Vp-p) | 5.0 |
| Current Consumption (mA/max) | 80 at Rated Voltage |
| Sound Pressure Level (dB/min) | 85 at 10cm at Rated Voltage |
| Coil Resistance (Ω) | 32 ± 3 |
| Operating Temperature (℃) | -20 ~ +70 |
| Storage Temperature (℃) | -30 ~ +80 |
| Condition by reflow soldering (℃) | 250±5℃/ within5sec |
| Condition by hand (℃) | 350±20℃ / within 5sec |

PS：Vp-p＝1/2duty , square wave

2﹒Typical Frequency Response Curve

TEL:886-2-2601-3311

FAX:886-2-2601-3898

NO.4 Lane 505, Zhongzheng Rd,. Linkou Shiang,Taipei, Taiwan 24445 . R.O.C

3﹒Dimensions and Material

3-1 Shape

### Unit : mm

3-2 Material

| Housing | LCP plastic resin (Color : Black) |
| --- | --- |
| Type Of Connection Terminals | SMD |
| Weight (Gram) | 0.6 |

4﹒Recommend Driving Circuit

The base current Ib should high enough so that it saturates the collector current of the transistor with the CB load.

TEL:886-2-2601-3311

FAX:886-2-2601-3898

NO.4 Lane 505, Zhongzheng Rd,. Linkou Shiang,Taipei, Taiwan 24445 . R.O.C

5. TESTING METHOD

．Standard Measurement conditions

Temperature:25±2℃  Humidity:45-60%

．Acoustic Characteristics

The oscillation frequency, current consumption and sound pressure are measured by the measuring instruments shown below.

TEL:886-2-2601-3311

FAX:886-2-2601-3898

NO.4 Lane 505, Zhongzheng Rd,. Linkou Shiang,Taipei, Taiwan 24445 . R.O.C

6. RELIABILITY

| ITEMS | METHOD OF TEST AND MEASUREMENTS | PERFORMANCE |
| --- | --- | --- |
| Coldness withstanding | After 98 hours of being exposed to -30℃ environment, should be returned to normal environment for 2 hours, then re-proceed to test. | No abnormality shall exist |
| Hotness withstanding | After 98 hours of being exposed to +80℃ environment, should be returned to normal environment for 2 hours, then re-proceed to test. | No abnormality shall exist |
| Humidity withstanding | After 98 hours of being exposed to 40℃ 95%RH environment in actual operation, should be returned to normal environment for 2 hours, then re-proceed to test. | No abnormality shall exist |
| Durability | Testing after 1,000 hours actual continuous operation. (at standard measurement conditions) | No abnormality shall exist |
| Drop withstanding | A natural drop from 75cm high down to the ground. | No abnormality shall exist |
| Vibration withstanding | Vibration of 2,000 cycles per minute, 2mm amplitude, applied in X, Y and Z directions for 30 minutes each. | No abnormality shall exist |

7. PACKAGE METHOD

- 1000pcs per  tape reel, Total  8 tape reels , total  8000pcs carton;

Volume: L*W*H=520*335*290mm

< 2 >N﹒W﹒：4.8KGS； G﹒W﹒：6.0KGS；

< 3 > RoHS Mark: